## Slide 1
Illegal Parking in Bus Stops
Revenue generation via fines & kerb fees
improved On-Time Performance of buses
Passenger-safety exposure
A self-funding enforcement & monetization programme
Public Transport Agency · Bus Performance Study · July 2026

## Slide 2
Executive summary
THE PROBLEM
346k
Annual Estimated Illegal Parking at 912 stops carrying 76% of peak arrivals
~1.5 %
Peak On-Time Performance Loss lost network-wide (60s per obstruction scenario)
2,900 h
Annual Bus Delay AVL data and an 11-stop field survey
THE FIX PAYS FOR ITSELF
AED 46M
Year-1 fine revenue (AED 200/violation, 56% ticket-to-cash) + kerb fees growing to 4.2M/yr
+98M
5-yr NPV @7% Hybrid fixed 512 stops + 20 portable + kerb monetization
< 1 year
Payback period Revenue declines only because deterrence works
CRITICAL SAFETY ISSUE
Passengers board and alight in live traffic lane (field photo)

## Slide 3
CRITICAL SAFETY ISSUE
Passengers step off into moving traffic
Field photo, 28 Jul 2026 — layby blocked by a private car; the bus serves the stop from the carriageway and the passenger alights on the road, not the kerb.
!
346,000 / year
obstructed arrivals — each one a potential boarding or alighting in the live lane
!
The most vulnerable pay first
elderly passengers, wheelchair users, parents with children — level kerb access is exactly what the layby exists to provide
!
Zero-distance near-misses
the door opens into the same lane cars use to overtake the stopped bus
!
A liability the Agency carries
every peer city (NYC, London, Singapore) criminalised bus-stop parking on safety grounds before revenue grounds

## Slide 4
Documented daily, across the network
Private car holds the layby — the bus loads in the traffic lane beside it
Taxi and van parked hard against the marked, signed bus stop (route F16)
Vans occupy the stop — the Al Quoz New Housing bus is forced to serve from the lane
Who blocks the stops Taxis & limousines labour/shuttle vans private cars 60 cases Average 3-hour morning at just 11 stops
All photos: PTA field observations, Jul 2026.

## Slide 5
The evidence: Morning Peak (7 to 10 AM), 11 stops
60
Average blocked-layby cases
(07:00–10:00)
1 in 21
AM-peak bus arrivals met
an obstructed layby
87.2%
baseline OTP that day
(38 routes, 72,679 stop events)
78.7%
OTP at Sharaf DG Metro —
worst stop, most blockages (8)
Chart: Blocked-layby cases by location (07:00–10:00, single day)
| Business Bay | Sharaf DG Metro | Burjuman | Al Jafliya | Naif Int. | Burj Nahar | Al Hana | Al Rigga | Salah Al Din | Emirates Twr | Al Khail
Cases per stop (3h) | 10 | 8 | 7 | 6 | 5 | 5 | 5 | 5 | 4 | 3 | 2
Cross-check AVL data (22 Jul 2026) confirms these stops carry 1,254 bus arrivals in the AM peak alone — and that late running already concentrates in peak hours.

## Slide 6
Network-wide: 912 stops carry the risk
Every stop in the GTFS network was scored on the surveyed hotspot profile: peak bus throughput plus metro-station or mall adjacency.
Tier | Stops | Definition | Share of peak arrivals | Annual blockages
High | 112 | Matches surveyed profile (metro/mall + heavy throughput) — survey-calibrated rate | 24% | ≈ 182,000
Medium | 400 | Next 400 by peak throughput — 50% of survey rate (assumption) | 36% | ≈ 134,000
Low | 400 | Following 400 — 25% of survey rate (assumption) | 16% | ≈ 30,000
Total | 912 | 4 in 10 network stops | 76% | ≈ 346,000
76%
of all peak bus arrivals happen
at these 912 stops
7.5
violations per stop per day
at High-tier stops
Biggest non-surveyed exposures: Ibn Battuta, Union Metro, Mall of the Emirates, Gold Souq, Dubai Mall Metro, ADCB Metro.

## Slide 7
What it costs the network every year
346,000
bus arrivals obstructed per year
(912 stops, both peaks)
2,900 h
of direct bus delay per year
(at 30 s per obstruction)
−0.85 pp
peak OTP lost network-wide
(30–60 s scenarios: −0.35 to −0.85)
Chart: Extra late trips per year by tier (60 s per obstruction)
| High tier | Medium tier | Low tier
Extra late trips | 11500 | 8500 | 1880
Why small delays matter OTP counts a trip late beyond +5 minutes. The damage lands on trips already 4–5 minutes behind — 12.7% of peak stop events. A 30-second obstruction tips 1 in 38 of the trips it touches over the line; at 60 seconds, 1 in 16.

## Slide 8
Enforcement pays: the violation-to-cash funnel
415,000
detectable violations / yr
cameras watch 24/7 — off-peak adds 20%
→
290,000
valid tickets (70%)
plate readable, stationary, de-duplicated
→
232,000
collected (80%)
at AED 200 per violation
→
AED 46M
gross revenue, year 1
declining by design as deterrence works
Chart: Revenue declines 25%/yr — because deterrence is working
| Year 1 | Year 2 | Year 3 | Year 4 | Year 5
Gross fine revenue (AED M) | 46.5 | 34.8 | 26.1 | 19.6 | 14.7
The honest pitch Fines finance the system in years 1–3. The permanent returns are OTP recovery, safe boarding — and kerb fees that grow as fines shrink.

## Slide 9
Option A — fixed cameras: invest where density pays
Tier | Capex | Revenue yr 1 | 5-yr NPV @7% | Payback
High — 112 stops | AED 4.5M | AED 24.4M | +56.6M | < 1 year
Medium — 400 stops | AED 16.0M | AED 18.0M | +22.6M | ~1 year
Low — 400 stops | AED 16.0M | AED 4.0M | −13.8M | never
Chart: 5-year NPV by tier (AED M)
| High | Medium | Low
5-yr NPV (AED M) | 56.6 | 22.6 | -13.8
Recommended Stop at High + Medium. 512 stops · AED 20.5M capex 5-yr NPV +79.2M · payback < 1 yr The Low tier's violation density is too thin to carry a fixed installation — leave it to the portable fleet.
Assumed: AED 40k/site capex, 5k/yr opex (benchmark; pre-RFP).

## Slide 10
Option B — portable cameras: small capex, follows
the problem
Chart: 5-yr NPV by fleet size, monthly rotation at High-tier stops (AED M)
| 20 units | 30 units | 40 units | 50 units
5-yr NPV (AED M) | 8.3 | 12.5 | 16.6 | 20.8
7.5
violations seen per
deployed camera per day
3.5×
daily revenue vs daily
all-in cost per unit
Economics per unit: ≈ AED 830/day collected vs ≈ AED 240/day cost (AED 15k capex + 60k/yr crew, vehicle, redeployment). Every fleet size is NPV-positive — value scales with units, and rotation adds a "cameras could be anywhere" deterrence halo that fixed sites lack. Trade-off: only 2–5% of stop-time covered, so OTP recovery is slower than fixed coverage.
Deployed at High-tier stops; deterrence decay 15%/yr under monthly rotation.

## Slide 11
Monetize the kerb: charge operators for legal use
Enforcement creates a licensed product to sell: managed, off-peak layby access (max 3-min dwell, geofence-verified) — billed by the same ANPR cameras, so marginal field cost is ~zero.
AED 2.4M / yr
Annual layby-access permits 2,000 licensed shuttle & coach vehicles × AED 1,200/yr — off-peak windows only, never during bus peaks
AED 1.8M / yr
Pay-per-use kerb fee 1,000 paid dwells/day × AED 5, ANPR-billed — the airport kerb-fee model applied to bus laybys
Chart: Kerb revenue ramps up as fines ramp down (AED M)
| Year 1 | Year 2 | Year 3 | Year 4 | Year 5
Kerb revenue (AED M) | 1.7 | 3.4 | 4.2 | 4.2 | 4.2
+10.2M NPV · payback year 2 · and unlike fines, this line grows: it converts today's violators into paying customers with a legal option, and becomes the programme's permanent revenue as deterrence shrinks the fine curve. Setup: AED 2M platform + 0.5M/yr admin (assumptions, adjustable).

## Slide 12
The 5-year money story — full programme
Fixed cameras at 512 High + Medium stops, 20 portable units, plus kerb monetization. All figures AED, undiscounted cash per year.
PHASE 1 — deploy High tier + portable
PHASE 2 — Medium tier + kerb permits
PHASE 3 — steady state: kerb fees replace fines
−22.8M
Start
capex: 512 fixed sites,
20 portable, kerb platform
+48.5M
Year 1
fines 46.8 + kerb 1.7
opex −4.3M
net +44.2M
+38.9M
Year 2
fines 35.5 + kerb 3.4
opex −4.3M
net +34.6M
+31.2M
Year 3
fines 27.0 + kerb 4.2
opex −4.3M
net +26.9M
+24.8M
Year 4
fines 20.6 + kerb 4.2
opex −4.3M
net +20.5M
+19.9M
Year 5
fines 15.7 + kerb 4.2
opex −4.3M
net +15.6M
BREAK-EVEN ~ MONTH 7
+119M
cumulative cash by end of year 5
+98M
net present value @ 7% discount
+0.85 pp
peak OTP recovered — the return that compounds

## Slide 13
Recommendation: the hybrid programme
Phase 1 · Months 0–6
Fixed cameras at 112 High-tier stops + 20 portable units.
Run the validation survey that firms Medium/Low rates.
Capex ≈ AED 4.8M.
Phase 2 · Months 6–18
Extend fixed coverage to the 400 Medium-tier stops.
Launch layby-access permits for licensed operators.
Grow portable fleet to 30–50. Capex ≈ AED 18M — funded by Phase 1 revenue.
Phase 3 · Year 2+
Scale pay-per-use kerb fees — the permanent revenue line.
Portable rotation covers the Low tier and emerging hotspots.
Publish OTP recovery; review AED 200 vs AED 500 federal fine.
+98M
5-yr NPV, full programme (AED)
+0.85pp
peak OTP recoverable network-wide
< 1 yr
payback on every element deployed
Fines are the financing bridge; kerb fees are the steady state. Both decline/grow exactly as compliance improves — while OTP and safety gains compound.

## Slide 14
Benchmarking: Every peer city has already moved
New York — MTA ACE
Bus-mounted cameras, escalating fines US$50–250
~5% faster buses, ~20% fewer collisions, ~30% fewer repeat violations
London — TfL
Bus stop clearways, CCTV-enforced 24/7, PCN £160
Near-universal kerb access; compliance underpins the iBus OTP regime
Singapore — LTA
Camera-equipped buses since 2008, ~S$150 fine
Sustained bus-lane and stop compliance
Sydney — TfNSW
Bus-zone offence ≈ A$390
Deterrence through penalty level
Dubai today: manual patrols only. This study models a conservative AED 200 fine — the federal schedule already allows AED 500 for stopping in a bus stop, which would scale every revenue figure ×2.5 and turn even the Low tier positive.

## Slide 15
Benchmarking: cities already charge for the kerb
Airports — SFO, LAX & most large US hubs
Kerb-access fees: US$2.50–5 per pick-up
Taxis, ride-hail and shuttles billed automatically via geofence/AVI — the direct template for ANPR-billed layby dwell fees
Smart loading zones — Pittsburgh, LA, Columbus, Aspen
Camera-billed per-minute commercial kerb use
Registered operators pay per minute, violators get fined — enforcement and monetization on the same sensor
Central London — Westminster
Paid coach bays & permits
Coaches pay for timed use of high-demand kerb bays via permit/app
Chicago & US CBDs
Ride-hail pick-up zone surcharges
Designated TNC zones carry a per-trip fee for kerb access rights
The pattern: the same camera that fines illegal use bills legal use. Cities monetise scarce kerb instead of only policing it — RTA's laybys at 912 high-demand stops are exactly that asset.

## Slide 16
Thank you